## Slide 1: Reconsideration of York Commons - East Lobe
Presented by V3 Companies
Greg Wolterstorff, P.E.

## Slide 2
CBBEL Comprehensive Flood Plan
Presentation 7/18/2011

## Slide 3
Crescent
38 Homes Impacted
Washington
63 Homes Impacted
Vallette/Swain
94 Homes Impacted
CBBEL Comprehensive Flood Plan
Presentation 7/18/2011

## Slide 4
Saylor/Jackson
104 Home Impacted
Spring/Harrison
17 Homes Impacted
CBBEL Comprehensive Flood Plan
Presentation 7/18/2011

## Slide 5
Crescent
All 38 Homes Removed
100-Yr Depth 19” Lower
Washington
0 of 63 Homes Removed
100-Year Depth – 0.84” Lower
Vallette/Swain
0 of 94 Homes Removed
100-Yr Depth – 0.72” Lower
York Commons
West Lobe Only
11-Ac Ft

## Slide 6
Table 1a – Homes Removed from Impact Cost Comparison
Proposed Alternative | Estimated Cost | Homes Removed from 100-Year Flood | Cost Per Home
York Commons – Both Lobes | $3.2 million | 52 | $61,500
York Commons – East Lobe Only | $1.8 million | 14 | $128,500
York Commons – West Lobe Only | $1.4 million | 38 | $36,800
Alternative #2A – Pump Capacity (Washington & Saylor/Jackson) | $19.2 million | 100 | $192,000
Alternative #4 – Pump Capacity (Swain/Vallette) | $11.5 million | 87 | $132,000

## Slide 7
Crescent
All 38 Homes Removed
100-Yr Depth 19” Lower
Washington
13 of 63 Homes Removed
100-Year Depth – 8” Lower
Vallette/Swain
1 of 94 Homes Removed
100-Yr Depth – 1” Lower
York Commons
Both Lobes
23-Ac Ft

## Slide 8
Table 1b – Homes Removed from Impact Cost Comparison
Proposed Alternative | Estimated Cost | Homes Removed from 100-Year Flood | Cost Per Home
York Commons – Both Lobes | $3.2 million | 52 | $61,500
York Commons – East Lobe Only | $1.8 million | 14 | $128,500
York Commons – West Lobe Only | $1.4 million | 38 | $36,800
Alternative #2A – Pump Capacity (Washington & Saylor/Jackson) | $19.2 million | 100 | $192,000
Alternative #4 – Pump Capacity (Swain/Vallette) | $11.5 million | 87 | $132,000

## Slide 9
Additional Costs
McKinley St Sewer –
9’x5’ Box to 10’x5’
2. Washington St Sewer - 11’x6’ Box to 12’x6’
3. 9% Capacity Increase in Two Lift Stations
4. Obtain 12 - 18 Ac-Ft of Compensatory Volume
Increase Cost = $600,000 to $1.5 M
Plus if Property Acquired = $3.25 M

## Slide 10
Table 2 – West Lobe & Both Lobes Cost Comparison
Proposed Alternative | Estimated Cost | Homes Removed from 100-Year Flood | Cost Per Home
York Commons – West Lobe Sewer Expansion Pump Expansion Compensatory Storage | $22.3 million To $26.9 million | 222* | $100,500 To $121,200
York Commons – Both Lobes Sewer Expansion Pump Expansion Compensatory Storage | $21.0 million To $22.1 million | 222 | $94,600 To $99,600
York Commons – East Lobe Only | $1.8 million | 14 | $128,500
York Commons – West Lobe Only | $1.4 million | 38 | $36,800
* Homes Removed - 38 Crescent, 52 Washington, 87 Swain/Vallette, 45 Saylor/Jackson

## Slide 11
Table 3 – Madison School Cost Comparison
Proposed Alternative | Estimated Cost | Homes Removed from 100-Year Flood | Cost Per Home
York Commons – West Lobe Sewer Expansion Pump Expansion Compensatory Storage | $22.3 million To $26.9 million | 222 | $100,500 To $121,200
York Commons – West Lobe Sewer Expansion Pump Expansion Compensatory Storage Madison School | $22.8 million To $27.2 million | 222 | $102,700 To $122,500
York Commons – Both Lobes Sewer Expansion Pump Expansion Compensatory Storage | $21.0 million To $22.1 million | 222 | $94,600 To $99,600
York Commons – Both Lobes Sewer Expansion Pump Expansion Compensatory Storage Madison School | $22.1 million To $23.1 million | 222 | $99,500 To $104,000

## Slide 12: Questions?
Presented by V3 Companies
Greg Wolterstorff, P.E.